## Slide 1: Nonparametric First Passage Time Distribution Estimation for Degradation Data with Random Effects
May 2025
Lochana Palayangoda, PhD
Assistant Professor of Data Science and Statistics
Department of Mathematical and Statistical Sciences
University of Nebraska at Omaha
LiDA 2025

## Slide 2: Highly reliable products last for long time but their performance subject to degradation over time
Year 0
Year 1
Year 2
Year 3
Degradation Data  Estimate the Lifetime
2
Threshold ()
2
  Light Output Degradation ()
  Time
  Experiment limit
First Passage Time =
First Passage Time (FPT) Distribution

## Slide 3: Parametric Lévy process based stochastic models are generally used for degradation modeling
Gamma process
𝑋_𝑡 "~ Gamma(" α𝑡,ν") "
Inverse Gaussian (IG) process
𝑋_𝑡~" Inverse Gaussian(" μ𝑡, λ𝑡^2 ")"
Gamma process
Inverse Gaussian (IG) process

## Slide 4: Fixed Effect versus Random Effect Random effect (heterogeneity) modeling accounts for unit-to-unit variability
Unit 1
Unit 2
Time
Fixed Effect
Degradation
Random Effect
Degradation
Time

## Slide 5: Studies on Parametric Degradation Data with Random Effects
Gamma Process with Random effects
Inverse Gaussian Process with Random Effects
Lawless and Crowder (2004); Tsai et al. (2012)
Peng (2015)

## Slide 6: Gamma Degradation Process with Random Effects
Gamma Process
Assume the rate parameter follows a probability distribution
First Passage Time (Failure Time) Distribution with Threshold Level
Notation:
is the F-distribution with degrees of freedom a and b
Lawless and Crowder (2004); Tsai et al. (2012)

## Slide 7: IG Degradation Process with Random Effects
IG Process
Assume that both mean and shape parameters follow a probability distribution
First Passage Time (Failure Time) Distribution with Threshold Level
Peng (2015)

## Slide 8: Empirical Saddlepoint Approximation (ESA)

## Slide 9: Studies on Nonparametric FPT Estimation
Empirical saddlepoint approximation for degradation data with Random Effects
Balakrishnan and Qin (2017)
Improved empirical saddlepoint approximation for degradation data fixed effects
Palayangoda et. al (2020)

## Slide 10: Studies on Nonparametric FPT Estimation with ESA
Develop an ESA approach to estimate the FPT distribution
Introduced procedures for both fixed and random effects
Effective mainly for the estimation of upper-percentiles
Improved the ESA method by Balakrishnan and Qin (2017)
Developed for only degradation data with fixed effects
Maintain the accuracy of the full FPT distribution.
Introduced the Conditional Random Imputation (CRImp) technique to apply the ESA with unequally spaced measurements

## Slide 11: ESA Method enables to estimate of the FPT distribution without any distributional assumptions
Saddlepoint Approximation
FPT Distribution
Degradation Data
Empirical Cumulant Generating Function of
Empirical Cumulant Generating Function of 𝑋_𝑡
Saddlepoint Approximation
FPT Distribution
Degradation Data
ESA method is a robust approach that can be used to avoid model misspecification errors (Palayangoda et al., 2020)
Balakrishnan and Qin (2019), Palayangoda et al. (2020)
Empirical CGF of Lévy process
is determined by solvingthe saddlepoint equation:

## Slide 12: Random Effects with Empirical Saddlepoint Approximation Method (Random ESA Method)
Propose a distribution-free
random effect method
Simulations
Applications

## Slide 13: Empirical Cumulant Generating Function for Random Effects
Empirical MGF for Degradation of unit
Empirical MGF of
Let random variable incorporate the unit-to-unit variability, and is the PDF of
Empirical Cumulant Generating Function (ECGF) of

## Slide 14: Weighting Methods for the ECGF for Random Effects
Equal Weight Method
Empirical Cumulant Generating Function (ECGF) of
Random Mean Method
Random Standard Deviation Method
Random Standardized Mean Method

## Slide 15: Weight ECGF is applied for saddlepoint approximation to obtain the FPT distribution with random effects
Apply ESA for Random Effects
FPT Distribution
Degradation Data with Random Effects
Evaluate ECGF of
Evaluate ECGF of 𝑋_𝑡
Select Weight Function
Select Weight Function 𝑓_𝑊 (𝑤)
Apply ESA for Random Effects
FPT Distribution
Degradation Data with Random Effects
is determined by solving the saddlepoint equation:

## Slide 16: FPT Distribution Estimation with Proposed ESA Method with Random Effects
is determined by solving saddlepoint equation:

## Slide 17: CRImp approach is applied when degradation data are collected with unequal time intervals
FPT Distribution
Degradation Data with Random Effects
Evaluate ECGF of
Evaluate ECGF of 𝑋_𝑡
Select Weight Function
Select Weight Function 𝑓_𝑊 (𝑤)
For each Unit Apply CRImp Algorithm
Make all degradation data equally spaced
FPT Distribution
Degradation Data with Random Effects
For each Unit Apply CRImp Algorithm
Make all degradation data equally spaced
CRImp – Conditional Random Imputation Technique
ECGF – Empirical Cumulant Generating Function
FPT – First Passage Time Distribution

## Slide 18: Monte Carlo Simulations

## Slide 19: Simulation Results shows that we can eliminate the model misspecification errors with ESA method for higher percentiles
Data Generated from Gamma
Data Generated from Inverse Gaussian

## Slide 20: Simulation Results shows that we can eliminate the model misspecification errors with ESA method for higher percentiles
Data Generated from Random Gamma Process

## Slide 21: Simulation Results shows that we can eliminate the model misspecification errors with ESA method for higher percentiles
Data Generated from Random IG Process

## Slide 22: Applications

## Slide 23: GaAs Laser Data Set in Meeker and Escobar (1998)
 | Random Gamma | Random IG | ESA Random BQ | ESA Equal Weight | ESA Mean | ESA Variance | ESA CV
10-th Percentile | 3858 | 3702 | - | 3617 | 3439 | 3510 | 3556
90-th Percentile | 6448 | 6296 | 6380 | 6414 | 6314 | 6346 | 6373
 | We only consider the measurements at time points {250, 500, 1000, 1750, 2000, 2500, 3250, 3500, 4000} | ESA Equal Weight* | ESA Mean* | ESA Variance* | ESA CV*
10-th Percentile |  | 3615 | 3607 | 3611 | 3615
90-th Percentile |  | 6458 | 6445 | 6458 | 6459

## Slide 24: A novel distribution-free approach is proposed to obtain the first passage time distribution with random designs for degradation data
Thank you! Questions
The Distribution-free ESA method is proposed to obtain the FPT with Random Effect
Monte-Carlo simulations show that the ESA method works well particularly for 10-th percentile and MTTF
The GaAs data set (Meeker and Escobar (1998)) is used to model with the proposed approach